Ford MUSTANG – EUROPEAN Specifications

PERFORMANCE

| Model | 0-100 km/h (0-62 mph) seconds* |
| --- | --- |
| Ford Mustang fastback 5.0-litre V8 manual | 4.8 |
| Ford Mustang fastback 2.3-litre EcoBoost manual | 5.8 |

ECONOMY**

| Model | Fuel consumption l/100 km (mpg) combined | CO2 g/km combined |
| --- | --- | --- |
| Ford Mustang fastback 5.0-litre V8 manual | 13.5 (20.9) | 299 |
| Ford Mustang fastback 5.0-litre V8 automatic | 12.0 (23.5) | 281 |
| Ford Mustang convertible 5.0-litre V8 manual | 13.6 (20.8) | 306 |
| Ford Mustang convertible 5.0-litre V8 automatic | 12.8 (22.1) | 289 |
| Ford Mustang fastback 2.3-litre EcoBoost manual | 8.0 (35.3) | 179 |
| Ford Mustang fastback 2.3-litre EcoBoost automatic | 9.8 (28.8) | 225 |
| Ford Mustang convertible 2.3-litre EcoBoost manual | 8.2 (34.4) | 184 |
| Ford Mustang convertible 2.3-litre EcoBoost automatic | 9.8 (28.8) | 225 |

BODY

| Construction | Unitised welded steel body, aluminium bonnet and front wings |
| --- | --- |
| Body Styles | Fastback and Convertible; Left-hand and Right-hand Drive |
| Final assembly location | Flat Rock, Michigan, USA |

ENGINE

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Configuration | Aluminium block and head | Aluminium block and heads |
| Intake manifold | Composite shell-welded with runner pack | Composite shell-welded with runner pack and charge motion control valves |
| Exhaust manifold | Three-port integrated into aluminium head | Stainless steel tubular manifold |
| Valvetrain | DOHC, four valves per cylinder, twin independent variable camshaft timing | DOHC, four valves per cylinder, twin independent variable camshaft timing |
| Valve diameter/lift | Intake 31 mm/8.31 mm Exhaust 30 mm/7.42 mm | Intake 37.3 mm/13 mm Exhaust 31.8 mm/13 mm |
| Pistons | Cast aluminium | Cast aluminium |
| Connecting rods | Forged steel | Forged steel |
| Ignition | Distributor-less with coil-on-plug | Distributor-less with coil-on-plug |
| Bore x stroke | 87.55 mm x 94 mm | 92.2 mm x 92.7 mm |
| Displacement | 2300 cc | 4951 cc |
| Compression ratio | 9.5:1 | 11.0:1 |
| Engine control system | PCM | PCM |
| Power | 317 PS (233 kW/312 bhp) @ 5500 rpm | 421 PS (310 kW/415 bhp) @ 6500 rpm |
| Torque | 432 Nm @ 3000 rpm | 530 Nm @ 4250 rpm |
| Fuel capacity | 59 L | 61 L |
| Fuel delivery | Direct injection | Sequential multiport electronic |
| Oil capacity | 5.7 L 5W-30 with filter (15,000-km service interval) | 7.6 L 5W-20 with filter (15,000-km service interval) |
| Cooling | Oil cooler and large capacity radiator | Oil cooler and large capacity radiator |

DRIVETRAIN

| Layout | Rear-wheel drive with limited-slip differential |
| --- | --- |

TRANSMISSION

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Standard | Six-speed manual with Hill Start Assist |
| Gear ratios |
| First | 4.236 | 3.657 |
| Second | 2.538 | 2.430 |
| Third | 1.665 | 1.686 |
| Fourth | 1.238 | 1.315 |
| Fifth | 1.00 | 1.00 |
| Sixth | 0.834 | 0.651 |
| Final drive | 3.31:1 | 3.55:1 |
| Optional | Six-speed automatic with paddle shifters |
| Gear ratios |
| First | 4.17 |
| Second | 2.34 |
| Third | 1.52 |
| Fourth | 1.14 |
| Fifth | 0.87 |
| Sixth | 0.69 |
| Final drive | 3.55:1 |

SUSPENSION

| Front | Double-ball-joint independent MacPherson strut and tubular stabiliser bar |
| --- | --- |
| Rear | Integral-link independent with coil springs, solid stabiliser bar, and twin-tube dampers (2.3-litre EcoBoost) or mono-tube dampers (V8) |

STEERING

| Type | Selectable Effort Electric Power Assisted Steering, rack-and-pinion gear |
| --- | --- |
| Ratio | 16:1 |
| Turning circle, curb-to-curb | 12.2 m |

BRAKES

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Type | Four-wheel power disc brakes with four-sensor, four-channel anti-lock braking system and AdvanceTrac electronic stability control | Four-wheel power disc brakes with four-sensor, four-channel anti-lock braking system and AdvanceTrac electronic stability control. Electronic line-lock |
| Front | 352 mm x 32 mm vented discs, four-piston 46 mm fixed aluminium callipers | 380 mm x 34 mm vented discs, Brembo six-piston 36 mm fixed aluminium callipers |
| Rear | 330 mm x 25 mm vented discs, single-piston 45 mm floating iron callipers, integral parking brake | 330 mm x 25 mm vented discs, single-piston 45 mm floating iron callipers, integral parking brake |

WHEELS AND TYRES

| Standard | 255/40 R19 Tyres, 19 inch x 9 inch aluminium wheels | Front: 255/40 R19 Tyres, 19 inch x 9 inch aluminium wheels Rear: 275/40 R19 Tyres, 19 inch x 9.5 inch aluminium wheels |
| --- | --- | --- |

DIMENSIONS

|  | Fastback | Convertible |
| --- | --- | --- |
| EXTERIOR |
| Wheelbase | 2720 | 2720 |
| Overall length | 4784 | 4784 |
| Overall width excluding mirrors | 1916 | 1916 |
| Overall width including mirrors | 2080 | 2080 |
| Overall width mirrors folded | 1956 | 1956 |
| Overall height | 1381 | 1394 |
| Track, front/rear | 1582/1655 | 1582/1655 |
| INTERIOR |
| Seating capacity | Four | Four |
| Front headroom | 955 | 956 |
| Front legroom – maximum | 1131 | 1131 |
| Front shoulder room | 1430 | 1430 |
| Front hip room | 1395 | 1395 |
| Rear headroom | 884 | 907 |
| Rear legroom | 777 | 783 |
| Rear shoulder room | 1327 | 1135 |
| Rear hip room | 1203 | 1111 |

WEIGHTS

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Manual Transmission | 1620 kg | 1651 kg |
| Automatic Transmission | 1617 kg | 1659 kg |

CAPACITIES

|  | Fastback | Convertible |
| --- | --- | --- |
| Passenger volume | 2392 L | 2287 L |
| Cargo volume | 408 L | 332 L |

STANDARD EXTERIOR EQUIPMENT

| 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- |
| Auto HID headlamps |
| Body-colour heated door mirrors with integrated turn signals |
| Dual Bright exhaust | Dual Bright exhaust with rolled polished tips |
| LED Tail Lamps |
| Rain Sensing Wipers |
| Rear Diffuser |

STANDARD INTERIOR EQUIPMENT

| 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- |
| Aluminium instrument panel accents and pedals |
| Ambient Lighting |
| Auto-dimming rear-view mirror |
| Bright door speaker, cup holder, air vent and instrument cluster surrounds |
| Dual-zone climate control |
| Illuminated sill plates |
| Leather handbrake |
| Leather seats |
| Nine-speaker sound system with amplifier |
| Premium door trim |
| SYNC 2 voice control connectivity system with 8-inch colour touch screen |
| Track Apps including Launch Control (V8 manual only), Line Lock (v8 only) accelerometer, acceleration timer and brake performance |

STANDARD SAFETY AND SECURITY

| 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- |
| Active Anti-Theft System with perimeter alarm |
| Active Glovebox knee airbag |
| Driver and front-passenger Personal Safety System |
| Driver knee airbag |
| Driver/passenger side-impact airbags |
| Dual front airbags |
| Electronic locking centre console |
| Emergency Assistance |
| Illuminated Entry |
| ISOFIX points |

OPTIONAL EQUIPMENT

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Europe Custom Package | 19-inch premium painted aluminium wheel with Luster Nickel finish |
|  | Bright door mouldings (Fastback only) |
|  | Ebony Black interior |
|  | Colour seat accents |
|  | Navigation |
|  | Reverse Parking Sensors |
|  | Shaker Pro audio system (12 speakers) |
|  | Unique door-trim |
|  | Unique instrument panel |
| Independent Options | 19-inch premium painted aluminium wheels with Luster Nickel finish |
|  | Climate Controlled seats |
|  | Recaro Leather Sport Seats (Fastback only) |
|  | Shaker Pro audio system (12 speakers) with navigation |
|  | Thatcham alarm |

INTERIOR COLOURS AND TRIM

| 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- |
| Ceramic leather |
| Dark Saddle leather |
| Ebony leather |
| Premium Ebony leather (EU Custom Pack only) |
| Ebony leather Recaro seats |

EXTERIOR COLOURS

|  | 2.3-litre EcoBoost | 5.0-litre Ti-VCT V8 |
| --- | --- | --- |
| Solid Colours | Black |
|  | Oxford White |
|  | Race Red |
|  | Competition Orange |
| Metallic Colours | Deep Impact Blue |
|  | Guard |
|  | Ingot Silver |
|  | Magnetic |
|  | Ruby Red |
| Tri-coat Colours | Triple Yellow |

*Ford test figures

**The declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

Specifications and equipment availability may vary according to individual market.