ford FOCUS RS – Preliminary Technical Specifications

PERFORMANCE AND ECONOMY

|  |  |  | Fuel consumption l/100 km (mpg) ØØ | Performance Ø |
| --- | --- | --- | --- | --- |
| Engine | Power (PS) | CO2 (g/km) | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h 0-62 mph (sec) |
| 2.3 EcoBoost 5-dr | 350 | 175 | 10.0 (28.2) | 6.3 (44.8) | 7.7 (36.7) | 266 (165) | 4.7 |

ØFord test figures. ØØThe declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

WEIGHTS

|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Max. Roof Load (kg) |
| --- | --- | --- | --- |
| 2.3 EcoBoost 5-dr | 1599 | 2025 | 75 |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90% fuel levels, subject to manufacturing tolerances and options, etc., fitted.

DIMENSIONS

| Overall length | 4390 |
| --- | --- |
| Overall width with mirror / folded mirror / without mirrors | 2010/1858/1823 |
| Overall height unladen (with base tyre) | 1472 |
| Wheelbase (mm) | 2647 |
| Front track (mm) | 1564 |
| Rear track (mm) | 1539 |
| Luggage capacity (litres) |
| 5-seat mode (laden to parcel shelf) | 260 |
| 2-seat mode (laden to roof) | 1045 |
| Luggage Compartment dimensions (mm) |
| Load opening height max | 615 |
| Load opening width max | 996 |
| Max loading height (to roof / to parcel shelf) | 692/396 |
| Loading width between wheelhouses | 1029 |
| Loading length at floor to 2nd row | 798 |
| Loading length to first row | 1461 |
| Lift over height at curb load condition (unladen) | 706 |
| Fuel tank capacity (litres) |
| Petrol (l) | 51 |
| Interior 1st row (mm) |
| Legroom (maximum with seat in rearmost mid-height position) | 1094 |
| Shoulder room | 1411 |
| Interior 2nd row (mm) |
| Headroom (without sunroof / with sunroof) | 963/962 |
| Legroom (nominal with front seat in 95% SAE position) | 848 |
| Shoulder room | 1336 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

STEERING AND SUSPENSION

| System | Electronic Power Assisted (EPAS) |
| --- | --- |
| Turning circle (m) | 11.8 kerb to kerb; 12.2 wall to wall |
| Max steering wheel turns | 2.0 |

CHASSIS

| Front suspension | MacPherson strut with semi-isolated subframe |
| --- | --- |
| Rear suspension | SLA independent rear axle with control blade |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Brembo four-piston monoblock calliper | Integrated park-brake, floating calliper |
| Disc dimensions (mm) | 350 x 25mm ventilated disc | 302 x 11mm solid disc |
| Piston calliper dimensions (mm) | 4 x 38mm diameter | 1 x 38mm diameter |

WHEELS & TYRES

|  | Wheels | Tyres |
| --- | --- | --- |
| Standard | 8 x 19 RS Design 20-spoke cast alloy | Michelin Pilot Super Sport 235/35 R19 |
| Optional | 8 x 19 RS Design 10-spoke forged alloy | Michelin Pilot Sport Cup 2 235/35 R19 |

ENGINE DATA

|  |  | 2.3-litre EcoBoost |
| --- | --- | --- |
| Type |  | Inline four cylinder petrol, turbocharged, transverse |
| Displacement | cm3 | 2,261 |
| Bore | mm | 87.6 |
| Stroke | mm | 94.0 |
| Compression ratio |  | 9.4:1 |
| Max power | PS (kW) | 350 (257) |
|  | at rpm | 6,000 |
| Max torque | Nm | 440 (470 on transient overboost) |
|  | at rpm | 2000-4500 |
| Valve gear |  | DOHC with 4 valves per cylinder |
| Cylinders |  | 4 in-line |
| Cylinder head |  | Cast aluminium |
| Cylinder block |  | Cast aluminium |
| Camshaft drive |  | Twin Independent Variable Cam Timing (Ti-VCT) |
| Crankshaft |  | Cast iron, 8 counterweights, 5 main bearings |
| Engine management |  | Bosch MEDG17-I4 |
| Fuel injection |  | High pressure direct injection; 200 bar injection pressure |
| Emission control |  | 3-way catalyst |
| Emission level |  | Euro Stage 6 |
| Turbocharger |  | Honeywell twin-scroll fixed geometry turbocharger |
| Lubrication system |  | Pressure-fed with mechanical oil pump |
| System capacity with filter | litres | 5.4 |
| Cooling system |  | Water pump with thermostat and valves, with thermal management system |
| System capacity incl heater | litres | 6.9 |
| Transmission/ Driveline |  | MMT6 6-speed manual, Ford Performance All-Wheel Drive |
| Gear ratios |  |
|  |  | 1: 3.231 x 4.063 2: 1.952 x 4.063 3: 1.321 x 4.063 4: 1.029 x 4.063 5: 1.129 x 2.955 6: 0.943 x 2.955 R: (1.423 x 3.231) x 2.955 |

POWER/TORQUE CURVE

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.