Ford FIESTA ST Specifications

PERFORMANCE AND ECONOMY

|  |  |  | Fuel consumption l/100 km (mpg) | Performance |
| --- | --- | --- | --- | --- |
| Engine | Power (PS) | CO2 (g/km) | Urban | Extra Urban | Combined | Max speed kph (mph) | 0-100 kph 0-62 mph (sec) | 50-100 kph 31-62 mph (sec)* |
| 1.6 EcoBoost (6-sp manual) | 182 | 138 | 7.9 (35.8) | 4.8 (58.9) | 5.9 (47.9) | 223 (139) | 6.9 | 6.4 |
| 1.6 EcoBoost (6-sp manual) | 200 | 140 | 8.2 (34.3) | 4.9 (57.6) | 6.1 (46.3) | 230 (143) | 6.7 | 5.2 |

* In 4th gear

WEIGHTS

| Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) |
| --- | --- | --- | --- | --- |
| 1163 | 1575 | N/A | N/A | N/A |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90% fuel levels, subject to manufacturing tolerances and options, etc., fitted.

Towing limits quoted represent the maximum towing ability of the vehicle at its Gross Vehicle Mass to restart on a 12 per cent gradient at sea level. The performance and economy of all models will be reduced when used for towing. Nose weight limit is a maximum of 50 kg on all models.  Gross Train Mass includes trailer weight

DIMENSIONS

| Dimensions (mm) | 3-dr |
| --- | --- |
| Exterior |  |
| Overall length | 3982 |
| Overall width with/without mirrors | 1978/1709 |
| Overall width with folded back mirrors | 1787 |
| Overall height | 1456 |
| Wheelbase | 2489 |
| Interior |  |
| Front headroom | 991 |
| Front max legroom (lowest rearmost seating posn) | 1111 |
| Front shoulder room | 1350 |
| Rear headroom | 953 |
| Rear legroom | 823 |
| Rear shoulder room | 1300 |
| Luggage capacity (litres)‡ |  |
| 5-seat mode, laden to package tray (with mini spare) | 276 |
| 5-seat mode, laden to package tray (with tyre repair kit) | 290 |
| 2-seat mode, laden to roof (with mini spare) | 960 |
| 2-seat mode, laden to roof (with tyre repair kit) | 974 |
| Fuel tank capacity (litres) |  |
| Petrol | 48 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

STEERING

| System | Electronic Power Assisted Steering (EPAS), rack-and-pinion, 2.32 turns lock-to-lock |
| --- | --- |
| Ratio | 13.69:1 |
| Turning circle (m) | 11.2 |

WHEELS AND BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Hydraulically operated dual-circuit system with diagonal distribution. Vented front discs, solid rear discs. Electronic four-channel anti-lock braking system (ABS) with electronic brake-force distribution (EBD) and Emergency Brake Assist (EBA) |
| Disc dimensions (mm) | 278 x 23 | 253 x 10 |
| Piston calliper dimensions (mm) | 54 | 34 |
| Wheels | 7.5J x 17 light alloy metal 5-spoke | 7.5J x 17 light alloy metal 5-spoke |
| Tyres | 205/40 R17 | 205/40 R17 |

CHASSIS

| Front | Rear |
| --- | --- |
| Independent suspension with McPherson struts supported by L-shaped lower wishbones connected to vehicle sub-frame. Separate load paths for spring and damper | Torsion beam suspension with progressive tracking control. Coil springs positioned under-floor with separate monotube shock absorbers |
| 3-mode Electronic Stability Control (ESC) and enhanced Torque Vectoring Control (eTVC) |

ENGINE DATA

|  |  | 1.6-litre EcoBoost |
| --- | --- | --- |
|  |  | 182 PS | 200 PS |
| Type |  | Inline four cylinder turbo petrol, transverse |
| Displacement | cm3 | 1596 |
| Bore | mm | 79.0 |
| Stroke | mm | 81.4 |
| Compression ratio |  | 10.1:1 |
| Max power -- steady state | PS kW) | 182 (134) | 200 (147) |
|  | at rpm | 5700 | 6000 |
| Max power -- transient overboost | PS kW) | 200 (147) | 215 (158) |
|  | at rpm | 5700 | 6000 |
| Max torque -- steady state | Nm | 240 | 290 |
|  | at rpm | 1600-5000 | 2500-4000 |
| Max torque -- transient overboost | Nm | 290 | 320 |
|  | at rpm | 2500-4000 | 2500 |
| Valve gear |  | DOHC with 4 valves per cylinder |
| Cylinders |  | 4 in line |
| Cylinder head |  | Cast aluminium |
| Cylinder block |  | Cast aluminium |
| Camshaft drive |  | Timing belt |
| Crankshaft |  | Cast iron |
| Engine management |  | Bosch |
| Fuel injection |  | High pressure direct fuel injection system with 6 hole injectors |
| Emission level |  | Euro Stage 6 |
| Turbocharger |  | Fixed geometry turbo with active wastegate and active compressor recirculation valve |
| Lubrication system |  | Pressure-fed with variable displacement pump and full flow oil filter |
| System capacity with filter | litres | 4.1 |
| Cooling system |  | Water pump with thermostat and valves, with thermal management system |
| System capacity | litres | 5.5 |
| Transmission |  | Durashift 6-speed (B6) manual |
| Gear ratios |  |
|  |  | 6th 0.690 5th 0.821 4th 1.032 3rd 1.357 2nd 2.048 1st 3.727 Reverse 3.818 Final Drive 3.824 | 6th 0.690 5th 0.821 4th 1.032 3rd 1.357 2nd 2.048 1st 3.727 Reverse 3.818 Final Drive 4.06 |

Note: The declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

# # #

About Ford Motor Company

Ford Motor Company is a global automotive and mobility company based in Dearborn, Mich. With about 199,000 employees and 67 plants worldwide, the company’s core business includes designing, manufacturing, marketing financing and servicing a full line of Ford cars, trucks, SUVs and electrified vehicles, as well as Lincoln luxury vehicles. At the same time, Ford is aggressively pursuing emerging opportunities through Ford Smart Mobility, the company’s plan to be a leader in connectivity, mobility, autonomous vehicles, the customer experience and data and analytics. For more information

regarding Ford, its products worldwide or Ford Motor Credit Company, visit www.corporate.ford.com.​​

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 53,000 employees at its wholly owned facilities and approximately 68,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 24 manufacturing facilities (16 wholly owned or consolidated joint venture facilities and 8 unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.