Ford EDGE Specifications

PERFORMANCE AND ECONOMY

|  |  |  |  | Fuel consumption l/100 km (mpg) ØØ | Performance Ø |
| --- | --- | --- | --- | --- | --- |
| Engine | Tyres | Power (PS) | CO2 (g/km) | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h 0-62 mph (sec) | 50-100 km/h 31-62 mph (sec)* |
| 2.0-litre TDCi (6-speed manual) | 235/55 R19 | 180 | 149 | 6.4 (44.1) | 5.4 (52.3) | 5.8 (48.7) | 200 (124) | 9.9 | 9.7 |
| 2.0-litre TDCi (6-speed PowerShift) | 255/45 R20 | 210 | 152 | 6.5 (43.5) | 5.5 (51.4) | 5.9 (47.9) | 211 (131) | 9.4 | n/a |

*In 4th gear. ØFord test figures. ØØThe declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

WEIGHTS

|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) | Max. Roof Load [kg] |
| --- | --- | --- | --- | --- | --- | --- |
| 2.0-litre TDCi 180 PS 6-speed manual | 1913 | 2505 | 4505 | 2000 | 750 | 75 |
| 2.0-litre TDCi 210 PS 6-speed PowerShift Auto | 1949 | 2555 | 4555 | 2000 | 750 | 75 |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90% fuel levels, subject to manufacturing tolerances and options, etc., fitted

Towing limits quoted represent the maximum towing ability of the vehicle at its Gross Vehicle Mass to restart on a 12 per cent gradient at sea level. The performance and economy of all models will be reduced when used for towing. Nose weight limit is a maximum of 90 kg on all models.  Gross Train Mass includes trailer weight

DIMENSIONS AND CAPACITIES

| Dimensions (mm) |
| --- |
| Overall length | 4808 |
| Overall width with mirror / folded mirror / without mirrors | 2184 / 1981 /1928 |
| Overall height unladen (with base tyre) | 1692 |
| Overall height unladen (with base tyre and roof rails) | 1707 |
| Minimum ground clearance (GVM) | 152 |
| Minimum ground clearance (kerb) | 203 |
| Wheelbase | 2849 |
| Front track | 1655 |
| Rear track | 1664 |
| Angles (degrees) |
| Approach angle degree (unloaded vehicle) | 18.8 |
| Departure angle (unloaded vehicle) | 22.4 |
| Ramp break over angle (unloaded vehicle) | 17.1 |
| Luggage capacity (litres) |
| 2-seat mode (laden to roof) | 1847 |
| 5-seat mode (laden to luggage cover) | 602 |
| 5-seat mode (laden to roof) | 800 |
| Luggage Compartment dimensions (mm) |
| Load opening height max (at vehicle centreline) | 794 |
| Load opening width (at floor) | 1178 |
| Cargo height (at vehicle centreline) | 802 |
| Loading width between wheelhouses | 1150 |
| Loading length at floor to 2nd row | 1071 |
| Loading length at floor to 1st row | 1918 |
| Lift over height at kerb load condition (unladen) | 754 |
| Fuel tank capacity (litres) |
| Diesel | 68.9 |
| Interior 1st row (mm) |
| Headroom | 1020 |
| Headroom with sunroof | 956 |
| Legroom | 1081 |
| Shoulder room | 1531 |
| Hip room | 1420 |
| Interior 2nd row (mm) |
| Headroom | 1023 |
| Headroom with sunroof | 962 |
| Legroom | 1030 |
| Shoulder room | 1536 |
| Hip room | 1461 |

STEERING AND SUSPENSION

| System | Rack and Pinion with Electronic Power Assisted Steering (EPAS), optional Ford Adaptive Steering (FAS) |
| --- | --- |
| Turning circle (m) | 11.9 |
| Max steering wheel turns | 2 turns lock-to-lock (vehicles equipped with FAS) |

CHASSIS

| Front suspension | Independent, MacPherson struts and L-shaped lower control arm with isolated subframe and stabiliser bar |
| --- | --- |
| Rear suspension | Independent integral-link suspension with isolated subframe and stabiliser bar |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Hydraulically operated dual-circuit system with diagonal distribution. Vented front and rear discs. Electronic four-channel anti-lock braking system (ABS) with electronic brake-force distribution (EBD), Electronic Stability System (ESP) and Emergency Brake Assist (EBA) |
| Disc/Drum dimensions (mm) | Ø316x32 | Ø316x11 |
| Piston calliper dimensions (mm) | 2x Ø44 | Ø38 |

WHEELS & TYRES

|  | Wheels | Tyres |
| --- | --- | --- |
| Standard | 19-inch X 8-inch | 235/55-R19 |
| Optional | 20-inch X 8.5-inch | 255/45-R20 |

ENGINE DATA

|  |  | 180 PS 2.0-litre TDCi (6-speed manual) | 210 PS 2.0-litre TDCi (6-speed PowerShift) |
| --- | --- | --- | --- |
| Type |  | Inline four cylinder turbo diesel | Inline four cylinder bi-turbo diesel |
| Displacement | cm3 | 1997 | 1997 |
| Bore | mm | 85.0 | 85.0 |
| Stroke | mm | 88.0 | 88.0 |
| Compression ratio |  | 16.7:1 | 16.0:1 |
| Max power | PS (kW) | 180 (132) | 210 (154) |
|  | at rpm | 3500 | 3750 |
| Max torque | Nm | 400 | 450 |
|  | at rpm | 2000-2500 | 2000-2250 |
| Valve gear |  | DOHC with 4 valves per cylinder | DOHC with 4 valves per cylinder |
| Cylinders |  | 4 in-line | 4 in-line |
| Cylinder head |  | Cast aluminium | Cast aluminium |
| Cylinder block |  | Cast iron | Cast iron |
| Camshaft drive |  | Belt driven cams with primary drive tensioner | Belt driven cams with primary drive tensioner |
| Crankshaft |  | Steel, 4 counterweights, 5 main bearings | Steel, 4 counterweights, 5 main bearings |
| Engine management |  | Ford Common Rail Diesel Engine Management System | Ford Common Rail Diesel Engine Management System |
| Fuel injection |  | Multipoint direct injection | Multipoint direct injection |
| Emission level |  | Euro Stage 6 | Euro Stage 6 |
| Turbocharger |  | Variable Nozzle, high mounted | Twin-sequential Borg Warner fixed-geometry |
| Cooling system |  | Ford Active Thermal Management System | Ford Active Thermal Management System |
| Transmission |  | 6-speed (MMT6) manual | 6-speed (MPS6) PowerShift automatic |
| Gear ratios |  |  |
|  |  | 1 - 3.583 2 - 1.864 3 - 1.156 4 - 0.816 5 - 0.886 6 -0.737 Reverse – 5.099 FD - 4.533 / 3.238 | 1 – 3.583 2 – 1.952 3 – 1.194 4 – 0.829 5 – 0.943 6 – 0.756 Reverse – 4.843 FD - 4.533 / 3.091 |

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

# # #

Ford Motor Company

Ford Motor Company is wereldwijd toonaangevend op het gebied van auto's en mobiliteit. Het bedrijf is gevestigd in Dearborn, Mich., Verenigde Staten. Het bedrijf heeft 199.000 werknemers en 67 fabrieken wereldwijd. De kerntaken zijn het ontwerpen, fabriceren, op de markt brengen, financieren en onderhouden van een volledig assortiment personenauto's, pick-ups, SUV's en elektrisch aangedreven auto's van het merk Ford. Ook het luxemerk Lincoln maakt deel uit van Ford. Daarnaast houdt Ford zich via Ford Smart Mobility ook intensief bezig met nieuwe mogelijkheden. Met dit plan streeft Ford ernaar om toonaangevend te zijn op het gebied van connectiviteit, mobiliteit, autonome auto's, de klantervaring en data analytics. Meer informatie over Ford, zijn internationale producten of over de Ford Motor Credit Company, vindt u op www.corporate.ford.com.

Ford Europa fabriceert, verkoopt en onderhoudt auto's van het merk Ford in 50 afzonderlijke markten en heeft ongeveer 53.000 werknemers in dienst. Joint ventures en zelfstandige activiteiten meegeteld, werken er ongeveer 68.000 mensen voor het bedrijf. Ford Europa bestaat uit Ford Motor Credit Company, Ford Customer Service Division en 24 productiefaciliteiten (16 eigen of geïntegreerde joint venture-faciliteiten en 8 zelfstandige joint venture-faciliteiten). De eerste auto's van Ford werden in 1903 naar Europa verscheept, hetzelfde jaar waarin Ford Motor Company is opgericht. De productie in Europa begon in 1911.

Voor meer informatie over Ford:

Ford Nederland B.V.

Afdeling Public Relations

Sebastiaan van de Pol

Telefoon: 020-5044778

E-mail: svandepo@ford.com

Mediasite: www.fordmediacenter.nl