BODY Construction Carbon fibre monocoque with integrated steel roll cage and aluminium substructure Body style Mid-engine, rear-wheel drive with active aerodynamics and suspension Final assembly location Markham, Ontario, Canada ENGINE 3.5L Twin Turbocharged EcoBoost V6 Configuration Aluminium block and heads Intake manifold Cast aluminium Exhaust manifolds Cast stainless steel Valvetrain Double overhead camshaft, four valves per cylinder, Twin-Independent Variable Camshaft timing, low-friction roller-finger-follower rocker arms Valve diameter/lift Intake: 37.4 mm / 9.96 mm Exhaust: 31.6 mm / 11.0 mm Pistons Cast aluminium Connecting rods Fully-machined forged steel Ignition Coil-on-plug Bore x stroke 92.51 mm x 86.7 mm Displacement 3,497 cc Compression ratio 9.0:1 Engine control system Ford PCM Horsepower (SAE) 647 hp @ 6250 RPM (U.S. values, European values pending certification) Torque (SAE) 550 lb-ft @ 5900 RPM (U.S. values, European values pending certification) Recommended fuel 98 RON Fuel capacity 57.5 litres Fuel delivery Sequential electronic direct and port fuel injection Oil capacity 14.5 litres Lubrication 4-stage external dry sump oil pump EPA-estimated fuel economy ratings European values TBD DRIVETRAIN Layout Rear-wheel drive with limited-slip differential TRANSMISSION: Getrag 7DCL750: Seven-Speed Dual-Clutch Transaxle Gear ratios 1st 3.397 2nd 2.186 3rd 1.626 4th 1.285 5th 1.029 6th 0.839 7th 0.634 Final drive 3.667 SUSPENSION Front Unequal length upper and lower control arms, pushrod/rocker-activated torsion bar/coil spring and electronically-adjustable DSSV® dampers; two-position ride height/spring rate system with additional front lift mode Rear Unequal length upper and lower control arms, pushrod/rocker-activated torsion bar/coil spring and electronically-adjustable DSSV® dampers; two-position ride height/spring rate system STEERING Type Hydraulic power-assisted rack-and-pinion Ratio 14.8:1 Turning circle, kerb-to-kerb 12.2 metres BRAKES Type Four-wheel power carbon ceramic matrix disc brakes with four-sensor, four-channel antilock braking system and AdvanceTrac® electronic stability control Front 394 mm x 36 mm, floating-type vented and cross-drilled discs, Brembo six-piston fixed aluminium callipers Rear 360 mm x 32 mm vented discs and cross-drilled discs, Brembo four-piston fixed aluminium callipers, electronically actuated Brembo spot calliper parking brake WHEELS AND TIRES Standard (F) 20 inch x 8.5 inch forged alloy wheels with 245/35 R20 Michelin Pilot Sport Cup 2 tyres Standard (R) 20 inch x 11.5 inch forged alloy wheels with 325/30 R20 Michelin Pilot Sport Cup 2 tyres Optional (F) 20 inch x 8.5 inch carbon fibre wheels with 245/35 R20 Michelin Pilot Sport Cup 2 tyres Optional (R) 20 inch x 11.5 inch carbon fibre wheels with 325/30 R20 Michelin Pilot Sport Cup 2 tyres DIMENSIONS EXTERIOR Wheelbase 2,710 mm Overall length 4,779 mm Overall width 2,003 mm (body) / 2,238 mm (mirrors extended) / 2,114 mm (mirrors folded) Overall height 1,109 mm (normal ride height); 1,063 mm (low ride height) Track: front / rear 1,694 mm /1,662 mm Ground Clearance 120 mm (normal ride height) 70 mm (low ride height) Approach Angle 9.5 degrees (normal) 13.0 degrees (front lift) Drag Coefficient 0.388 (V-Max Mode) Frontal Area 1.779 m2 CdA 0.690 m2 INTERIOR Seating capacity 2 Front headroom 908 mm Front legroom, maximum 1,122 mm Front shoulder room 1,238 mm Front hip room 1,145 mm DRY WEIGHT Coupe 1,385 kg CAPACITIES Passenger volume 1,226 litres Cargo volume 11.3 litres PERFORMANCE Top Speed 347 km/h (216 mph) For editorial use only. Information correct at time of publication. Check media.ford.com for updates.