ALL-NEW Ford FIESTA ST Specifications

Performance and Economy

| Fiesta 3dr and 5dr |  |  |  |  |
| --- | --- | --- | --- | --- |
|  |  |  | Fuel consumption l/100 km (mpg) | Performance |
| Engine | Power PS | CO2 g/km | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h 0-62 mph sec | 50-100 km/h 31-62 mph sec* |
| 1.5 EcoBoost | 200 | 136 | 7.6 (37.2) | 5.1 (55.4) | 6.0 (47.1) | 232 (144) | 6.5 | 6.1 |

* In 4th gear

WEIGHTS AND DIMENSIONS

Weights

| Fiesta ST |  |  |
| --- | --- | --- |
|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) |
| Fiesta ST 5dr | 1283 | 1655 |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90 per cent fuel levels, subject to manufacturing tolerances and options, etc., fitted.

Dimensions

| Fiesta ST | 5dr |
| --- | --- |
| Dimensions (mm) |  |
| Exterior |  |
| Overall length | 4068 |
| Overall width with/without/folded mirrors | 1941/1735/1783 |
| Overall height | 1469 |
| Wheelbase | 2493 |

| Interior |  |
| --- | --- |
| Front headroom | 992 |
| Front max legroom | 1125 |
| Front shoulder room | 1347 |
| Rear headroom | 955 |
| Rear legroom | 835 |
| Rear shoulder room | 1301 |
| Luggage capacity (litres) |  |
| 5-seat mode | 311 |
| 2-seat mode, laden to roof (with tyre repair kit) ‡ | 1093 |
| Fuel tank capacity (litres) |  |
| Petrol | 42 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

DRIVER ASSISTANCE TECHNOLOGIES

Adjustable Speed Limiter

Auto High Beam

Blind Spot Information System

Driver Alert

Hill Launch Assist

Lane Keeping Aid

Lane Keeping Alert

Rear-view camera and parking sensors

Selectable Drive Modes

Traffic Sign Recognition

SAFETY

Airbags: driver front, driver side, passenger front, passenger side, curtain x 2

Electronic Emergency Brake Assist

Electronic Stability Control

Front and rear outer seat load limiters and pre-tensioners

Driver’s seatbelt with locking tongue

ISOFIX child seat hard points

Passenger airbag deactivation with indicator

Rear seatbelt reminder

STEERING

| System | Rack and pinion with Electronic Power Assisted Steering (EPAS) |
| --- | --- |
| Ratio | 12:1 |
| Turning circle (m) | 11.0 kerb-to-kerb |

CHASSIS

| Front suspension | Independent suspension with MacPherson struts, Tenneco twin-tube RC1 dampers and 22.5 mm diameter anti-roll bar |
| --- | --- |
| Rear suspension | 1,400 Nm/degree twistbeam rear suspension with toe-correcting bush. Force vectoring springs. Tenneco mono-tube RC1 dampers |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Hydraulically operated dual-circuit system with diagonal distribution. Vented front discs. Solid rear discs. Electronic four-channel anti-lock braking system (ABS) with electronic brake-force distribution (EBD), Electronic Stability System (ESP) and Emergency Brake Assist (EBA) |
| Disc dimensions (mm) | 278 x 23 | 253 x 12 disc |
| Piston dimensions (mm) | Ø54 | Ø36 |

WHEELS & TYRES

| Alloy wheels |  |
| --- | --- |
| 17-inch x 7.5-inch | Michelin Pilot Super Sport 205/45 R17 |
| 18-inch x 7.5-inch | Michelin Pilot Super Sport 205/40 R18 |

AERODYNAMICS

| Model (3dr and 5dr) | Cd | A (m2) |
| --- | --- | --- |
| ST | 0.341 | 2.15 |

ENGINE

|  |  | 1.5-litre EcoBoost |
| --- | --- | --- |
| Type |  | Inline three cylinder turbo petrol, Ti-VCT, transverse |
| Displacement | cm3 | 1497 |
| Bore | Mm | 84.0 |
| Stroke | Mm | 90.0 |
| Compression ratio |  | 9.7:1 |
| Max power | PS (kW) | 200 (147) |
|  | at rpm | 6000 |
| Max torque | Nm | 290 |
|  | at rpm | 1600-4000 |
| Valve gear |  | DOHC with 4 valves per cylinder, twin independent variable cam timing |
| Cylinders |  | 3 in-line, cylinder deactivation technology |
| Cylinder head |  | Cast aluminium |
| Cylinder block |  | Cast aluminium |
| Camshaft drive |  | Low friction Belt-in-Oil with dynamic tensioner |
| Crankshaft |  | Cast iron, 6 counterweights, 4 main bearings |
| Engine management |  | Bosch MG1CS016 with CAN-Bus and individual cylinder knock control. FGEC software |
| Fuel injection |  | High-pressure direct fuel injection with 6 hole injectors (DI) plus 3 low-pressure individual port injectors (PFI) |
| Emission level |  | Euro Stage 6 |
| Turbocharger |  | Continental RAAX low-inertia turbocharger |
| Lubrication system |  | Two-stage variable displacement oil pump |
| System capacity with filter | Litres | 5.25 |
| Cooling system |  | Single thermostat |
| System capacity incl heater | Litres | 6.15 |
| Transmission |  | 6-speed manual with optional Quaife Limited Slip Differential |
| Gear ratios |  | 6th 0.651 5th 0.775 4th 0.971 3rd 1.290 2nd 1.952 1st 3.583 Reverse 3.333 FDR 4.313 |

# # #

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

Note: The declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel-efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

From 1 September 2017, certain new vehicles will be type-approved using the World Harmonised Light Vehicle Test Procedure (WLTP) according (EU) 2017/1151 as last amended, which is a new, more realistic test procedure for measuring fuel consumption and CO2 emissions. From 1 September 2018 the WLTP will fully replace the New European Drive Cycle (NEDC), which is the current test procedure. During NEDC Phase-out, WLTP fuel consumption and CO2 emissions are being correlated back to NEDC. There will be some variance to the previous fuel economy and emissions as some elements of the tests have altered i.e., the same car might have different fuel consumption and CO2 emissions.