NEW Ford FIESTA ACTIVE Specifications

Performance and Economy

| Fiesta Active |  |  |  |  |
| --- | --- | --- | --- | --- |
|  |  |  | Fuel consumption l/100 km | Performance |
| Engine* | Power PS | CO2 g/km | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h (0-62 mph) sec | 50-100 km/h (31-62 mph) sec* |
| 1.0 EcoBoost | 100 | 114 | 5.9 (47.9) | 4.4 (64.2) | 5.0 (56.5) | 181 (112) | 11.0 | 11.6 |
| 1.0 EcoBoost auto | 100 | 139 | 7.8 (36.2) | 5.2 (54.3) | 6.1 (46.3) | 177 (110) | 12.8 | N/A |

All engines feature Auto-Start-Stop unless indicated

* In 4th gear

WEIGHTS AND DIMENSIONS

Weights

| Fiesta Active (without openable panorama roof) |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) | Nose weight (kg) | Roof load (kg) |
| 1.0 EcoBoost 100 PS | 1241 | 1685 | 2685 | 1000 | 620 | 65 | 50 |
| 1.0 EcoBoost 100 PS Auto | 1284 | 1690 | 2690 | 1000 | 640 | 45 | 50 |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90 per cent fuel levels, subject to manufacturing tolerances and options, etc., fitted.

Towing limits quoted represent the maximum towing ability of the vehicle at its Gross Vehicle Mass to restart on a 12 per cent gradient at sea level. The performance and economy of all models will be reduced when used for towing.  Gross Train Mass includes trailer weight

Dimensions

| Dimensions (mm) | Active |
| --- | --- |
| Exterior |  |
| Overall length | 4068 |
| Overall width with/without/folded mirrors | 1941/1756/1783 |
| Overall height | 1498 |
| Wheelbase | 2493 |
| Front track | 1513 |
| Rear track | 1476 |
| Front overhang | 857 |
| Rear overhang | 718 |
| Min ground clearance (unloaded) | 152 |
| Min ground clearance (loaded) | 130 |
| Interior |  |
| Front headroom | 992 |
| Front max legroom | 1125 |
| Front shoulder room | 1347 |
| Rear headroom | 955 |
| Rear legroom | 835 |
| Rear shoulder room | 1301 |
| Luggage capacity (litres) |  |
| 5-seat mode, laden to package tray (with tyre repair kit) | 311 |
| 2-seat mode, laden to roof (with tyre repair kit) ‡ | 1093 |
| Fuel tank capacity (litres) |  |
| Petrol/Diesel | 42/40 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

DRIVER ASSISTANCE TECHNOLOGIES

Adaptive Cruise Control

Adjustable Speed Limiter

Auto High Beam

Blind Spot Information System

Cross Traffic Alert

Forward Collision Warning

Rear Park Aid (sensors)

Rear parking camera

Hill Launch Assist

Lane Keeping Aid

Lane Keeping Alert

Pre-Collision Assist with Pedestrian Detection

Traffic Sign Recognition

SAFETY

Airbags: driver front, driver side, passenger front, passenger side, curtain x 2

Electronic Emergency Brake Assist

Electronic Stability Control

Front and rear outer seat load limiters and pre-tensioners

Driver’s seatbelt with locking tongue

ISOFIX child seat hard points

Passenger airbag deactivation with indicator

Rear seatbelt reminder

STEERING

| System | Rack and pinion with Electronic Power Assisted Steering (EPAS) |
| --- | --- |
| Ratio | 14.6:1 |
| Turning circle (m) | 10.3 kerb-to-kerb |

CHASSIS

| Front suspension | Independent suspension with MacPherson struts, L-shaped lower control arm, steering gear and hollow stabiliser bar mounted on subframe. Unique steering knuckle geometry. Hydraulic rebound stopper |
| --- | --- |
| Rear suspension | Twistbeam rear suspension with toe-correcting bush |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Hydraulically operated dual-circuit system with diagonal distribution. Vented front discs. Rear drums. Electronic four-channel anti-lock braking system (ABS) with electronic brake-force distribution (EBD), Electronic Stability System (ESP) and Emergency Brake Assist (EBA). Optional autonomous emergency braking (AEB) as part of Pre-Collision Assist with Pedestrian Detection |
| Disc/Drum dimensions (mm) | Ø262 x 23 | Ø 202.8 drum |
| Piston dimensions (mm) | Ø54 | Ø 20.64 drum |

WHEELS & TYRES

| Alloy wheels |  |
| --- | --- |
| 17-inch x 7-inch | 205/45-R17 |

AERODYNAMICS

| Model (5dr) | Engine | Cd | A (m2) |
| --- | --- | --- | --- |
| Active | 1.0-litre Ecoboost | 0.328 | 2.16 |

PETROL ENGINES

|  |  | 1.0-litre EcoBoost (100 PS) manual | 1.0-litre EcoBoost (100PS) automatic |
| --- | --- | --- | --- |
| Type |  | Inline three cylinder turbo petrol, Ti-VCT, transverse | Inline three cylinder turbo petrol, Ti-VCT, transverse |
| Displacement | cm3 | 998 | 998 |
| Bore | Mm | 71.9 | 71.9 |
| Stroke | Mm | 82.0 | 82.0 |
| Compression ratio |  | 100 PS 10.5:1 | 10.0:1 |
| Max power | PS (kW) | 100 (74) | 100 (74) |
|  | at rpm | 4500-6500 | 4500-6500 |
| Max torque | Nm | 170 | 170 |
|  | at rpm | 1500-4000 | 1500-4000 |
| Valve gear |  | DOHC with 4 valves per cylinder, twin independent variable cam timing | DOHC with 4 valves per cylinder, twin independent variable cam timing |
| Cylinders |  | 3 in line | 3 in line |
| Cylinder head |  | Cast aluminium | Cast aluminium |
| Cylinder block |  | Cast iron | Cast iron |
| Camshaft drive |  | Low friction Belt-in-Oil with dynamic tensioner | Low friction Belt-in-Oil with dynamic tensioner |
| Crankshaft |  | Cast iron, 6 counterweights, 4 main bearings | Cast iron, 6 counterweights, 4 main bearings |
| Engine management |  | Bosch MED17 with CAN-Bus and individual cylinder knock control. FGEC Software | Bosch MED17 with CAN-Bus and individual cylinder knock control. FGEC Software |
| Fuel injection |  | High pressure direct fuel injection with 6 hole injectors | High pressure direct fuel injection with 6 hole injectors |
| Emission level |  | Euro Stage 6 | Euro Stage 6 |
| Turbocharger |  | Continental low inertia turbo | Continental low inertia turbo |
| Lubrication system |  | Electronically controlled variable displacement oil pump for improved fuel economy | Electronically controlled variable displacement oil pump for improved fuel economy |
| System capacity with filter | Litres | 4.6 | 4.6 |
| Cooling system |  | Split cooling system with 2 thermostats | Split cooling system with 2 thermostats |
| System capacity incl heater | Litres | 5.8 | 5.8 |
| Transmission |  | 6-speed manual | 6-speed torque converter automatic |
| Gear ratios |  |  |  |  |  |
|  |  | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 3.941 | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 3.941 | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 3.941 | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 4.353 | N/A |

# # #

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

Note: The declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel-efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

From 1 September 2017, certain new vehicles will be type-approved using the World Harmonised Light Vehicle Test Procedure (WLTP) according (EU) 2017/1151 as last amended, which is a new, more realistic test procedure for measuring fuel consumption and CO2 emissions. From 1 September 2018 the WLTP will fully replace the New European Drive Cycle (NEDC), which is the current test procedure. During NEDC Phase-out, WLTP fuel consumption and CO2 emissions are being correlated back to NEDC. There will be some variance to the previous fuel economy and emissions as some elements of the tests have altered i.e., the same car might have different fuel consumption and CO2 emissions.